## Slide 1: STARS 2024 CPU Architecture

## Slide 2: Goals
Design and prototype a CPU with the follow components:
  Instruction Decoder/Control Unit
  ALU
  Program and Data Memory
  Registers
  Program Counter
  Peripherals:
    Display
    Keyboard?

## Slide 3: Goals
Implement the following commands in Assembly
Add/subtract
NOT, XOR, OR, AND
Shift left/right
Load to register/memory
Branch/Jump

## Slide 4: Goals
Possible apps/games to implement
  Pong
  Snake
  Tetris

## Slide 5: Model: RISC-V
Open source
31 internal registers
Add more stuff later

## Slide 6: Team Roles
Michael – Top Level Design, Program Counter
Andy – Control Unit (and decoder)
Mary – ALU
Dhruv – Registers/Memory
Travis – Peripherals (Display and keyboard)

## Slide 7: Top Level Design

## Slide 8: Control Unit & Decoder
Decoder:
Parse Instruction in to addresses, Opcodes, and data inputs to be used accordingly
Control Unit:
Enable relevant control signals based on Opcode

## Slide 9: Immediate Generator
Imm Gen:
Generate Immediate values if necessary and send immediate values to ALU

## Slide 10: Control Unit & Decoder Test Cases
Control Unit Test Cases
Input all valid Opcodes, validate control signal outputs
Input invalid Opcode, check for error
Decoder Test Cases
Input all instruction types with register addressees, validate correct addresses
Input instruction without register address, check for garbage output

## Slide 11: Immediate Generator Test Case
ImmGen Test Cases
Input all instruction types with an immediate value, validate correct immediate
Ensure no immediate is generated if instruction doesn’t include an immediate

## Slide 12: ALU
Input:
(operands)
-opA [31:0]
-opB [31:0]
(select signals)
-opcode[6:0]
-func3[2:0]
-func7[6:0]
Output:
-ALU result [31:0]
-0 flag
-don't care flags
-less than flags
-greater than flags
-equal/not equal flags
RTL:

## Slide 13: ALU
Pseudo Code:
ALU Control Unit:
if(opcode=1100011)
if(func3=000)
ALU control input = BEQ
if(func3=001)
ALU control input=BNE
if(opcode=0110011)
if(func3=000)
if(func7=0000000)
ALU control input=ADD
(....define the ALU control input for each
of the operations based on the value
of the opcode, func3 and func7…)
ALU:
case(ALU control input)
  ADD: ALU result = rs1+ rs2 ( opA + opB )
  flag 0 =0
  flag less than = 0
  flag greater than = 0
  flag don’t care = 0
  flag equal to /~ not equal to =0
  ADDI: ALU result = rs1+imm (opA + opB)
  flag 0 =0
  flag less than = 0
  flag greater than = 0
  flag don’t care = 0
  flag equal to /~ not equal to =0
  (....all operations are executed
  based on the ALU control input)

## Slide 14: ALU
Test Cases:
-all possible combination of opcode, func3 and func7 ( 26 combinations)
(make tasks for the operations)
-different corner cases for operands (add, and, xor, etc.)
(assign variable value to each operand)
all 0s
all 1s
all 5s
all As
pattern 0000 FFFF
pattern FFFF 0000
pattern AAAA 5555
pattern 5555 AAAA
-error checking for undefined combinations of opcode, func3 &func7 -> assign value
-check generation of correct flags

## Slide 15: Registers
Register RTL and Psuedocode

## Slide 16: Registers
Test Cases
Reset: check all registers are set to 0
With write_enable off, try writing register: should be no change
With write_enable on, try writing to a register: check for correct value
Write random values to all registers, try reading all registers: check data_read is correct
  Do twice
Reset check again

## Slide 17: Memory

## Slide 18: Program Counter
RTL Diagram and Input/Output

## Slide 19: Program Counter
Logic and Test Cases

## Slide 20: Peripherals

## Slide 21: Expected Obstacles

## Slide 22: Future Plans
Error correction?